## Slide 1: ARM® AMBA® AXI Advanced eXtensible Interface

## Slide 2: Topics
Overview of AXI
AXI architecture and features
Channel definitions and signals
Handshaking process
Basic AXI transactions
Types of Access (Atomic Accesses)
Ordering model (Transaction ID tags)
AXI4 & AXI4 Lite

## Slide 3: Overview of AXI

## Slide 4: System-On-Chip (SoC)
ARM A-15
AXI
Interconnect
USB
Memory
controller
PCIe Express
AXI
AHB
AXI
AXI
interface

## Slide 5: AXI Overview
Protocol basics
On-chip communication protocols
Connects multiple masters and slaves with AXI interconnect.
Supports Features:
  Burst write & Read transactions
  Out of order transactions,
  Parallel Write & Read transactions
  Over lapped transactions;
  Align & Unaligned transfers;
  protected and locked transfers
Phased transactions
Write transaction
  WR addr phase
  WR data phase
  WR response phase
Read transaction
  RD addr phase
  RD data & response phase
Signals classified in channels
AW, W, B, AR, R
Handshaking
Each channel has valid & ready
signal.
AWVALID = 1 @ posedge clk meaning master driving valid information on WR address channel signals.
AWREADY = 1 (slave driven) meaning slave ready to accept master given addr & ctrl info.
At clock posedge, when both AWVALID and AWREADY ‘1’ indicate completion of transfer.

## Slide 6: Topics
Overview of AXI
AXI Architecture and Features
Channel definitions and Signals
Handshaking process
Basic AXI transactions
Types of Access (Atomic Access)
Ordering Model (Transaction ID tags)
AXI4 & AXI4 Lite

## Slide 7: Architecture

## Slide 8: Terminology
AXI : Advanced eXtensible Interface (Interface divided into 5 channels)
Protocol : Set of rules.
Channel : Physical transmission medium (wires) to carry signals.
Signal : It’s an electric current or electromagnetic field that carries
information from one place (source) to another (destination).
Master : Initiates transactions.
Slave : receives and responds to transactions.
Interface : A point where two blocks meet and interact.
Interconnect : a device that allows to connect multiple masters and multiple slaves.

## Slide 9: Architecture
AXI is burst-based protocol, where transactions with only start address issued.
Address/Control issued ahead of actual data transfer.
Interface divided into 5 channels.

## Slide 10: Interface and Interconnect
Each master should be able to initiate transaction to each of slaves with use of interconnect.
Interconnect connects multiple masters to multiple slaves.
Interconnect is slave device for masters & master device for
Slaves
AXI Interface
Source: M.S. Sadri, Zynq Training

## Slide 11: Features

## Slide 12: Terminology
Transaction : Multiple transfers of data or an entire burst of transfers.
Transfer : A single exchange of information, with one valid and ready
handshake.
Beat : An individual data transfer within an AXI burst.
Burst : A transaction where multiple data items are transferred based
upon a single address.
Aligned : Each data transfer is aligned to the size of the transfer. E.g.: 32-bit transfer aligned to 4-byte boundaries (0, 4, 8, C).
Unaligned : A data access performed to an address which is not aligned to the size of the access. E.g.: A 32-bit data packet that starts at a byte address of 0x1002 is not aligned to the natural 32-bit address boundary.
Multiple outstanding addresses : Master able to provide transaction addresses without waiting for earlier transactions to complete.
Out of order transaction : Transactions to faster memory regions can
complete without waiting for last transaction to slower memory regions
Data Interleaving : Masters producing write data sequence to same slave but data not arriving each clock, interleave to avoid idle cycles on bus.

## Slide 13: Features
Burst Write and Read transactions.
Separate address/control and data phases.
Separate Read and Write data channels.
unaligned data transfers using byte strobes.
  Ex: Accessing 32-bit data starting at address 0x2
Issues multiple outstanding addresses
  ID signals
Out of order transaction and Data Interleaving
  ID signals

## Slide 14: Topics
Overview of AXI
AXI Architecture and Features
Channel Definitions and Signals
Handshaking Process
Basic AXI Transactions
Types of Access (Atomic Access)
Ordering Model (Transaction ID tags)
AXI4 & AXI4 Lite

## Slide 15: Channel Definitions

## Slide 16: Channel Definition
Each channel is independent and use two-way flow
control
VALID
  Asserted when valid data or control information available on channel.
READY
  Asserts when receiver can accept the data.
LAST
  Asserts while the final data completes

## Slide 17: AXI Signals

## Slide 18: AXI Signals

## Slide 19: Write Address Channel Signals
Source: ARM AMBA AXI Protocol v1.0: Specification

## Slide 20: AXI Signals

## Slide 21: Write Data Channel Signals
Source: ARM AMBA AXI Protocol v1.0: Specification

## Slide 22: AXI Signals

## Slide 23: Write Resp Channel Signals
Source: ARM AMBA AXI Protocol v1.0: Specification

## Slide 24: AXI Signals

## Slide 25: Read Address Channel Signals
Source: ARM AMBA AXI Protocol v1.0: Specification

## Slide 26: AXI Signals

## Slide 27: Read Data + Resp Channel Signals
Source: ARM AMBA AXI Protocol v1.0: Specification

## Slide 28: Topics
Overview of AXI
AXI Architecture and Features
Channel Definitions and Signals
Handshaking Process
Basic AXI Transactions
Types of Access (Atomic Access)
Ordering Model (Transaction ID tags)
AXI4 & AXI4 Lite

## Slide 29: Handshaking Process

## Slide 30: Handshake Process
Source: ARM AMBA AXI Protocol v1.0: Specification
Information moves
only when
  Source is Valid
  Destination is Ready
On each channel the master or slave can limit the flow
Very flexible

## Slide 31: Write channel handshaking
Master provides awvalid to show information valid on write addr channel.
Slave gives awready indicating
address information accepted.
Master provides wvalid to say information is valid in write data channel.
Slave gives wready indicating write data information accepted.
BVALID from slave shows valid information on write response channel
Master gives BREADY indicating write response information accepted.

## Slide 32: Read channel handshaking
Master provides arvalid to show information valid on read addr channel.
Slave gives arready indicating read
address information accepted.
Slave gives rvalid indicating valid information on read data & response channel.
Master provides rready saying read data & response information accepted.

## Slide 33: Dependencies between channel handshake signals
Write data can appear before Write address
Write data appear in the same cycle as the address
Read data always come after Read address
Write response always come after write data
Write dependency
Slave mustn't give read BRESP unless write addr & data phase completes.
Read dependency
No read data by slave unless read address phase completes.
Slave doesn’t need to wait for ARVALID assertion
Source: ARM AMBA AXI Protocol v1.0: Specification

## Slide 34: Topics
Overview of AXI
AXI Architecture and Features
Channel Definitions and Signals
Handshaking Process
Basic AXI Transactions
Types of Access (Atomic Accesses)
Ordering Model (Transaction ID tags)
AXI4 & AXI4 Lite

## Slide 35: AXI Transactions

## Slide 36
Read Transaction
+ Read Resp

## Slide 37: Read Bursts
Source: AMBA® AXI Protocol v 1.0 Specification, ARM, 2003.
Read Address Channel
Read Data Channel
The slave keeps the RVALID signal LOW until the read data is available.
Slave asserts RLAST for final data transfer in a burst indicating last data item
has been transferred.

## Slide 38: Overlapping Read Bursts
Source: AMBA AXI Protocol v 1.0 Specification, ARM, 2003.
A master can drive another burst address (B) after first addr accepted by slave.
First addr allows slave to process data for the second burst in parallel with the
completion of the first burst (RLAST, D(A2))

## Slide 39: Write Transactions

## Slide 40: Write Burst
Source: AMBA® AXI Protocol v 1.0 Specification, ARM, 2003.
Write Address `Channel
Write Response Channel
Write Data Channel
Source: AMBA AXI Protocol v 1.0 Specification, ARM, 2003.

## Slide 41: Addressing Options

## Slide 42: Burst Operation[5]
Burst length
1 beat
2 beats
16 beats
Undefined length
4 beats
8 beats
SIZE
Word halfword
……
Burst
Transfer
………
………

## Slide 43: Burst Transfer Type

## Slide 44: AXI Burst Transfer
 | D11 | D12 | D13 | D14 | D21 | D22 | D23 | D31
ADDRESS
DATA
AXI
A11 | A21 | A31 |  | A21 |  | A31
Start address
Multiple Data

## Slide 45: Burst Control signals
Every transaction must have the number of transfers.
No component can terminate a burst early to reduce the no. of data transfers.
Source: AMBA AXI Protocol v 1.0 Specification, ARM, 2003.

## Slide 46
Burst Type
Source: AMBA AXI Protocol v 1.0 Specification, ARM, 2003.

## Slide 47: Address calculations

## Slide 48: Burst address
Addresses of transfers within a burst:
Address of first transfers in a burst:
𝐴𝑑𝑑𝑟𝑒𝑠𝑠_1 = 𝑆𝑡𝑎𝑟𝑡_𝐴𝑑𝑑𝑟𝑒𝑠𝑠
Address of any transfer after first transfer in a burst:

## Slide 49: Burst address
Wrap_Boundary variable extended to get wrapping boundary:
Address of first transfers in a burst:
Address of any transfer after first transfer in a burst:

## Slide 50: INCR

## Slide 51: Find the address of each transfer in a burst
AWBURST = INCR
AWSIZE = 2
AWLEN = 3
AWADDR = 23C0
Bus_Size = 32 bits Solution Start_Address => 23C0
Number_Bytes => 2 AWSIZE => 2 2 = 4
Burst_Length => AWLEN + 1 = 3 + 1 = 4
Aligned_Address = INT(23C0/4) x 4 = 8F0 x 4 = 23C0
Address_1 = Start_Address = 23C0
Address_N = Aligned_Address + (N-1) x Number_Bytes
Address_2 = 23C0 + (2 - 1) x 4 = 23C4
Address_3 = 23C0 + (3 - 1) x 4 = 23C8
Address_4 = 23C0 + (4 - 1) x 4 = 23CC
Address : 23C0 , 23C4 , 23C8, 23CC

## Slide 52: Fixed

## Slide 53: Burst address (Fixed)
AWBURST = FIXED
AWSIZE = 1
AWLEN = 4
AWADDR = 44B0
Bus Size = 32 bits
Start_Address = 44B0 Number_Bytes = 2AWSIZE = 21 = 2 Burst_Length = AWLEN + 1 = 4 + 1 =5
Aligned_Address = INT(Start_Address/Number_Bytes) x Number_Bytes
= INT(44B0/2) x 2 = 2258 x 2 = 44B0

## Slide 54: Burst Address (Fixed…)
Since, it’s a Fixed Burst , so the Address will be same for each
transfer i.e.
Address_1 = 44B0
Address_2 = 44B0
Address_3 = 44B0
Address_4 = 44B0
Address_5 = 44B0

## Slide 55: Wrap

## Slide 56: Burst Address (WRAP)
AWBURST = WRAP
AWSIZE = 1
AWLEN = 2
AWADDR = A242
Bus Size = 32-bits
Start_Address = A242 Number_Bytes = 2AWSIZE = 21 = 2 Burst_Length = AWLEN + 1 = 2 + 1 =3
Aligned_Address = INT(A242/2) x 2 = 5121 x 2 = A242

## Slide 57: Burst Address (WRAP…)
Wrap_Boundary = (INT(A242/( 2 X 3))) X (2 X 3) = A242 Address_N=Wrap_Boundary+(Num_Bytes x Burst_Len)
Address_1 = A242
Address_2 = A242 + (2 - 1) x 2 = A244
Address_3 = A242 + (3 - 1) x 2 = A246
Address_4 = A242 + (4 - 1) x 2 = A248
Address : A242 , A244 , A246

## Slide 58: Additional Control Information

## Slide 59: Cache Support
Support for system level caches and other
performance enhancing components
  Bufferable (B) bit, ARCACHE[0] and AWCACHE[0]
  Cacheable (C) bit, ARCACHE[1] and AWCACHE[1]
  Read Allocate (RA) bit, ARCACHE[2] and AWCACHE[2]
  Write Allocate (WA) bit, ARCACHE[3] and AWCACHE[3]

## Slide 60: Cache Support
Cacheable Bit
  Write : a number of different writes can be merged
together.
  Read : a location can be pre-fetched or can be
fetched just once for multiple read transactions
Read Allocate Bit
  If the transfer is a read and it misses in the cache then it should be allocated
Write Allocate Bit
  If the transfer is a write and it misses in the cache then it should be allocated

## Slide 61: Cacheable Write – Sparse Strobes
64-bit write data bus
63 56 55 48 47
40 39
32 31
24 23
16 15
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
8 7
0
WSTRB
0
0
0
1
1
0
0
1
Cacheable Bit
Write : a number of different writes can be merged together
ARM11-MPCore processor and L220 Level 2 cache controller use sparse strobes. This is due to the fact that they use a merging write buffer. If the application writes several bytes at address 0x0, 0x3, 0x4, the write buffer will be drained using a 64- bit transfer, and strobes will be 0b00011001 and the AXI slave must only update the bytes that are enabled.

## Slide 62: Cache Encoding

## Slide 63: Protection Unit Support
To support complex system design, for the interconnect and other devices in the system to provide protection against illegal transactions
Normal or privileged, ARPROT[0] andAWPROT[0]
  Low High
Secure or non-secure, ARPROT[1] andAWPROT[1]
  Low High
Data or instruction, ARPROT[2] andAWPROT[2]
  Low High

## Slide 64: Topics
Overview of AXI
AXI Architecture and Features
Channel Definitions and Signals
Handshaking Process
Basic AXI Transactions
Types of Access (Atomic Access)
Ordering Model (Transaction ID tags)
AXI4 & AXI4 Lite

## Slide 65: Atomic Access

## Slide 66: Atomic Accesses
Source: ARM AMBA AXI Protocol v1.0: Specification

## Slide 67: Normal / Privileged (`b00)
Used by some masters to indicate processing mode.
A privileged processing mode has a greater level of access within a system.

## Slide 68: Exclusive Access (`b01)
0 1 2 3 4 5
Master2 Write
Cycle 1
Cycle 2
0 1 2 3 4 5
0 1 2 3 4 5
Cycle 3
Master1 Exclusive Read
Master 1Exclusive Write
Exclusive Write success Response : EXOKAY
Exclusive Write fail
Response : OKAY
Semaphore type without locking
the bus access
Exclusive Read success Response : EXOKAY
Exclusive Read fail Response : OKAY

## Slide 69: Locked Access
Interconnect makes sure only one specific master is allowed access to the slave region until an unlocked transfer from the same master completes.
Purpose of use for longer and undisturbed transfers

## Slide 70: Response Signals
Accessed reached slave but
slave gives error to master
No slave present at transaction address interconnect responsible for decode error

## Slide 71: Topics
Overview of AXI
AXI Architecture and Features
Channel Definitions and Signals
Handshaking Process
Basic AXI Transactions
Types of Access (Atomic Access)
Ordering Model (Transaction ID tags)
AXI4 & AXI4 Lite

## Slide 72: Ordering Model

## Slide 73: Ordering Model
AXI protocol enables out-of-order transaction completion and issuing of multiple outstanding addresses.
These features help maximize data throughput and system efficiency.
All transactions with same ID must be ordered, but there is no restriction on the ordering of transactions with different IDs.

## Slide 74: Ordering Model [1]
Multiple Outstanding Address
  Master is able to provide transaction addresses without waiting for earlier transactions to complete.
Write data Interleaving
  If two masters generate write data sequence to the same slave, but write data doesn't arrive every clock cycle.
  Instead of waiting for a data sequence to complete before other sequence starts, AXI system can interleave write data sequences avoiding idle cycles on the bus.
[1] AMBA AXI Protocol v 1.0 Specification, ARM, 2003.

## Slide 75: Read Ordering
At master interface, read data from read transactions with same ARID value must arrive in same order in which master issued addresses.
Data from read transactions with different ARID values can return in any order and it is also acceptable to interleave the read data of transactions with different ARID fields.

## Slide 76: Read Data Interleaving[5]

## Slide 77: Normal Write Ordering
If a slave does not support write data interleaving the master must issue the data of write transactions in the same order in which it issues the transaction addresses.
Write data does not support out-of-order transactions but support data interleaving.

## Slide 78: Write Data Interleaving[5]
Write data interleaving enables a slave interface to accept interleaved write data with different AWID values.
Figure: Write data Interleaving

## Slide 79: Out of Order Transaction
Transactions to faster memory regions can complete without waiting for previous transaction to slower memory regions.
Fast slaves may return data ahead of slow slaves

## Slide 80: Aligned Transfer
40 39
32 31
24 23
16 15
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
8 7
0
7
6
5
4
3
2
1
0
F | E | D | C | B | A | 9 | 8
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
7
6
5
4
3
2
1
0
F | E | D | C | B | A | 9 | 8
Address: 0x00
Transfer size: 32 bits Burst type: incrementing Burst length: 4 transfers
WSTRB
0
0
0
0
0
1
1
0
WSTRB
0
1
0
1
0
0
0
0
For wrapping burst type, all transfers are aligned transfers
64-bit write data bus
63 56 55 48 47

## Slide 81: Unaligned Transfer
40 39
32 31
24 23
16 15
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
8 7
0
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
17 | 16 | 15 | 14 | 13 | 12 | 11 | 10
F | E | D | C | B | A | 9 | 8
F | E | D | C | B | A | 9 | 8
WSTRB
1
0
0
0
0
0
0
0
WSTRB
0
0
0
0
1
1
1
0
Address: 0x07
Transfer size: 32 bits Burst type: incrementing Burst length: 4 transfers
For incrementing burst type, fist transfer can be unaligned transfers, but the rest transfers are aligned transfers
64-bit write data bus
63 56 55 48 47

## Slide 82: Write Strobes
40 39
32 31
24 23
16 15
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
8 7
0
64-bit write data bus
63 56 55 48 47
WSTRB
1
0
1
0
0
1
0
0
WSTRB Write strobes, signal indicates which byte lanes to update in memory.
One strobe for each eight bits of the write data bus.
WDATA : 8 – 1024 bits wide, WSTRB : 1 – 128 bits wide

## Slide 83: Topics
Overview of AXI
AXI Architecture and Features
Channel Definitions and Signals
Handshaking Process
Basic AXI Transactions
Types of Access (atomic accesses)
Ordering Model (AXI ID transaction)
AXI4 & AXI4 Lite

## Slide 84: AXI4

## Slide 85: AXI Interfaces
Source: M.S. Sadri, Zynq Training

## Slide 86: AXI4 Features
Support for cache coherency and enforced ordering.
Support for burst lengths up to 256 beats.
Support for Quality of Service signaling.
Support for multiple region interfaces.
AXI4 does not support locked transactions.

## Slide 87: Write Response Dependencies
The AXI4 protocol requires that the write response for all transactions must not be given until the clock cycle after address acceptance
Write Response Dependencies

## Slide 88: AXI4-Lite

## Slide 89: AXI4-Lite
Key functionality of AXI4-Lite operation.
all transactions are of burst length of 1
all data accesses use full width of the data bus
Supports a data bus width of 32-bit or 64-bit.
all accesses are Non-modifiable, Non-bufferable
Exclusive accesses are not supported.
EXOKAY response is not supported on the read
data and write response channels
Length, Burst, Size related signals are not supported.
Bus Width can be 32/64 bit and supports strobe.

## Slide 90: AXI4-Lite
No support data interleaving, the burst length is
defined as 1.
Does not support AXI IDs. Meaning, all transactions must be in order, and all accesses use a single fixed ID value.
Supports multiple outstanding transactions, but a slave can restrict this by the appropriate use of the handshake signals.

## Slide 91: AXI4-Lite Signals

## Slide 92: AXI4-Lite applications
Simple, low-performance peripherals
  General Purpose Input Output (GPIO).
    It’s a port used to connect any peripheral based on requirement where same port is used as input and output.
  Universal Asynchronous Receiver Transmitter (UART Lite)

## Slide 93: References
[1]
[2]
[3]
[4]
[5]
AMBA AXI Protocol v 1.0 Specification, ARM, 2003. AMBA Specification, Rev 2.0, ARM, 1999.
AMBA 4 AXI4-Stream Protocol Version 1.0 http://infocenter.arm.com/help/topic/com.arm.doc.set.amba https://www.slideshare.net/AzadMishra1/axi-protocol-55779579

## Slide 94: Thank you